## Slide 1
Construction and Evaluation of the HEV Control Algorithm using a Black-Box simulator
❇︎Nariaki Tateiwa1, Nozomi Hata1, Akira Tanaka1, Takashi Nakayama1, Akihiro Yoshida1, Takashi Wakamatsu1, Katsuki Fujisawa2
2019/3/28
The 4th IMI-ISM-ZIB MODAL Workshop Mathematical Optimization and Data Analysis @ The Institute of Statistical Mathematics, Tokyo, Japan
1Graduate School of Mathematics, Kyushu University, Fukuoka, Japan 2Institute of Mathematics for Industry, Kyushu University, Fukuoka, Japan & AIST-Tokyo Tech Real World Big-Data Computation Open Innovation Laboratory, Tokyo, Japan
Notes: Thank you for introduction and give me a opportunity to take a presentation today.
My name is Nariaki Tateiwa and I‘m a graduate student at Kyushu University in Japan.
The subject of my presentation is Construction and Evaluation of the HEV Control Algorithm using a Black-Box simulator.
Today, I’d like to talk about the way to optimize hybrid electric vehicle control.
This is a collaborative research with Toyota Motor Corporation.

## Slide 2: HEV Technology Explained
https://www.toyota-europe.com/world-of-toyota/feel/environment/better-air/hybrid-vehicle/howHybridworks
EV driving mode is driving with only motors
HV driving mode is driving with engine and motors
Notes: HEV has an engine and motors as a power source.
HEV has 2 driving mode,
We call EV driving mode driving …
By changing the output ratio of the engine and motors and switching HV and EV driving mode according the situation like this figure, HEV can drive more efficient than the car with only engine.

## Slide 3: Outline
Background and Problem Setting
Our Proposed Algorithm
  Local Optimization (Optimize in a part of Driving Cycle)
  Global Optimization (Optimize in a whole of Driving Cycle)
  Reduce Calculation Time
Numerical Experiments
Notes: Here is the outline of my presentation.
First, I talk about
Nest, I explain
Finally, I show the result of Numerical experiments

## Slide 4: Outline
Background and Problem Setting
Our Proposed Algorithm
  Local Optimization (Optimize in a part of Driving Cycle)
  Global Optimization (Optimize in a whole of Driving Cycle)
  Reduce Calculation Time
Numerical Experiments
Notes: Here is the outline of my presentation.
First, I talk about
Nest, I explain
Finally, I show the result of Numerical experiments

## Slide 5: Model Based Development
Powertrain of
Developing vehicle
Powertrain
Simulator
modeling
evaluating
Configuration design
Selection of engine and motor type
Numerous candidates of the powertrain system
best!
Notes: The model based development is a mainstream in the field of the development of new vehicles.
In model based development, we model a powertrain of vehicle and generate a powertrain-simulator, and evaluate the performance of the simulator instead of the original powertrain.
In the development stage, the developers should consider the numerous candidates of the configuration of the powertrain due to the based configuration design and selection of engine and motor.
and they have to find the best configuration of the powertrain from these.
Therefore, it is important to evaluate each candidate of the configuration fast and at low cost.
Next, I explain how to evaluate the performance of powertrain simulator.

## Slide 6: How to Evaluate the Simulator?
Simulator
Target Engine Torque
Target Motor Torque
WLTC Driving Cycle (30 minute)
input
Measure the fuel consumption when the vehicle virtually travels on the computer by using the simulator
Drive to follow the target velocity of Driving Cycle
output
State of vehicle
Notes: When we evaluate the performance of the simulator,
we measure the fuel …
the lower figure shows the WLTC Driving Cycle, and this is the vehicle speed pattern about 30 minute, and this is world standard driving cycle.
To control the vehicle using simulator, we input the target engine torque and motor torque.
The greater we input engine torque, the greater engine shaft speed is.

## Slide 7: How to Evaluate the HEV Simulator?
SOC-constraints (SOCState of battery Charge)
Approach final SOC to initial SOC
Keep SOC (constant value) overall of Driving Cycle
initial SOC 16 %
final SOC 16 %
Transition of SOC
Measure the fuel consumption when the vehicle virtually travels on the computer by using the simulator
Drive to follow the target velocity of Driving Cycle
Notes: In the case of HEV simulator, we should add two other SOC constraints.
SOC means the battery remaining quantity.
First constraint is we should …, for example if we start to drive with 16% SOC, we should end to drive with 16% SOC.
Another is that we should always keep SOC is greater than or equal a constant value for the sake of the electric equipment of vehicle.
In the case of HEV simulator, we should add two other SOC constraints.
SOC is the state of charge.
First constraint is …, for example if we start to drive with 16.3% SOC, we should end to drive with 16.3% SOC.
Another is that we should keep SOC is greater than or equal a constant value 𝛽 for the sake of the electric equipment of vehicle.

## Slide 8: How to Evaluate the HEV Simulator?
Important points to drive the Driving Cycle efficiently
When should we operate the engine in Driving Cycle?
Engine Torque
SOC
HV
EV
HV
EV
Notes: There are 2 important points to drive the Driving Cycle efficiency are
When…
EV driving mode is driving only motor, and HV driving mode is driving with a engine and motors.
Basically, in the HV driving mode, vehicle charge the buttery, and in the EV driving mode vehicle use the buttery, so we hove to combine the HV and EV driving mode well to satisfy the SOC-constraints.

## Slide 9: How to Evaluate the HEV Simulator?
Important points to drive the Driving Cycle efficiently
When should we operate the engine in Driving Cycle?
Where should we set the engine operating point?
Engine Torque [Nm]
Engine Shaft Speed [rpm]
Fuel Consumption Map [g/kWh]
sweet spot
Notes: The engine output and fuel consumption are mainly determined by the engine torque and the engine shaft speed.
This figure is the example of the fuel consumption map. The lower the value, the more the engine work efficiency.
The lowest value area of map is the optimal operating points of the engine, and we call this sweet spot. However the engine output at the sweet spot is much higher than the energy which is needed during normal traveling, so it is difficult to operate always the engine at the sweet spot.

## Slide 10: Previous Work to Evaluate the Simulator
Parameter tuning for one candidate takes a lot of time
Search region is limited by controller
Simulator
Candidates
Regard a simulator as a black box for flexibility in the configuration
Setting the Rule-based controller
Chose a configuration of the powertrain
Parameter Tuning
Drive by optimized controller
Optimized Rule-based controller
parameter tuning
Rule-based controller
velocity ≥ (km/h) & SOC ≤ %  high HV driving
velocity ≥ (km/h) & SOC > %  low HV driving
velocity < a (km/h)  EV driving
…
Notes: I explain how the previous work evaluates the simulator
First, setting the rule-based controller as shown in lower box. a and b are parameter

## Slide 11: Previous Work to Evaluate the Simulator
Parameter tuning for one candidate takes a lot of time
Search region is limited by controller
Rule-based controller
velocity ≥ (km/h) & SOC ≤ %  high HV driving
velocity ≥ (km/h) & SOC > %  low HV driving
velocity < a (km/h)  EV driving
…
Setting the Rule-based controller
Chose a configuration of the powertrain
Parameter Tuning
Drive by optimized controller
Optimized Rule-based controller
parameter tuning
Simulator
Candidates
Regard a simulator as a black box for flexibility in the configuration
Notes: Next, chose a …
We regard a simulator…
We regard a simulator as a black box means we use only the input and output of simulator,
and we don’t see the contents of simulator.

## Slide 12: Previous Work to Evaluate the Simulator
Setting the Rule-based controller
Chose a configuration of the powertrain
Parameter Tuning
Drive by optimized controller
Optimized Rule-based controller
parameter tuning
Rule-based controller
velocity ≥ (km/h) & SOC ≤ %  high HV driving
velocity ≥ (km/h) & SOC > %  low HV driving
velocity < a (km/h)  EV driving
…
Simulator
Candidates
Regard a simulator as a black box for flexibility in the configuration
Parameter tuning for one candidate takes a lot of time
Search region is limited by controller
Notes: Third, we do the parameter tuning in the controller for the simulator we chosed

## Slide 13: Previous Work to Evaluate the Simulator
Setting the Rule-based controller
Chose a configuration of the powertrain
Parameter Tuning
Drive by optimized controller
Optimized Rule-based controller
parameter tuning
Rule-based controller
velocity ≥ (km/h) & SOC ≤ %  high HV driving
velocity ≥ (km/h) & SOC > %  low HV driving
velocity < a (km/h)  EV driving
…
Simulator
Candidates
Regard a simulator as a black box for flexibility in the configuration
Parameter tuning for one candidate takes a lot of time
Search space is limited by controller
Notes: There two problem,
first ,second
the aim of our study is overcoming these problems.

## Slide 14: Purpose of Our Study
Input Driving Cycle, Simulator (Black box)
Output
Target engine and motor torques at each time that maximize fuel efficiency
Constraints
1. velocity target velocity of Driving Cycle (at each time point)
2. SOC (at each time point)
3. initial SOC final SOC (overall of Driving Cycle)
1. maximizes fuel economy efficiency
2. takes small calculation time
3. without controller
Construct a HEV control algorithm with a black-box simulator that
Notes: Summarize, the purpose of out study
without controller in order not to limit the search space
is nearly equal

## Slide 15: Outline
Background and Problem Setting
Our Proposed Algorithm
  Local Optimization (Optimize in a part of Driving Cycle)
  Global Optimization (Optimize in a whole of Driving Cycle)
  Reduce Calculation Time
Numerical Experiments
Notes: Here is the outline of my presentation.
First, I talk about
Nest, I explain
Finally, I show the result of Numerical experiments

## Slide 16: Outline of Solving Strategy
Local
Optimize some vehicle controls in a part of the Driving Cycle while changing the conditions
Global
Obtain vehicle control in the whole of Driving Cycle by solving the constrained shortest path problem on the State Transition Graph
Construct State Transition Graph
Discretize Driving Cycle and State of Vehicle
with no controller
Notes: I briefly explain the overview of our proposed algorithm.
We divide the problem into small problems by discretize Driving Cycle and states of vehicle.
we optimize some optimal …
next, we construct State Transition Graph based the result of the local optimization.
By solving the constrained shortest path problem on the State Transition Graph,
we select the local control for each sections

## Slide 17: Solving Strategy
Discretize the Driving Cycle and the state of vehicle
Velocity
…
Driving Cycle
State of vehicles
section 1
section 2
…
section 3
Discretize
Set States clusters by the driving mode and the amount of SOC
HV state
0% ≤ SOC ≤ 10%
EV state
0 %≤ SOC ≤ 10%
HV state
10% < SOC ≤ 20%
EV state
10% < SOC ≤ 20%
Notes: First of our algorithm, we discretize Driving Cycle into some sections, and set states clusters H1 to Hm …
SOC amount affects the battery charging efficiency
we are going to obtain the optimal controls for each section. Based on these local controls, we aim to obtain the global optimal control overall of Driving Cycle.
And we classify the state of vehicles into M state classes, to .
First, we construct a graph which represents the transition of state of vehicle, SOC, and fuel consumption. We call this graph State Transition Graph.
We discretize the Driving Cycle into several sections, and we are going to obtain the optimal controls for each section. Based on these local controls, we aim to obtain the global optimal control overall of Driving Cycle.
And we classify the state of vehicles into M state classes, 𝐻_1 to 𝐻_𝑀.

## Slide 18: Solving Strategy
Construct State Transition Graph ;
Nodes represent state clusters of vehicle
Edges represents the transitions of the state of vehicle, SOC and fuel consumption in the section
is the minimum fuel consumption under
SOC) in a section is fixed
State cluster at the start and end points are fixed
the change amount of
Section
Section
Section
Edge has two type of weight; (, = (SOC, Fuel)
※SOCState of battery Charge
Notes: nodes prepare the nodes corresponding to the state classes at each section.
Then, we generate the edge which represents the change amount of SOC and fuel consumption when we drive in the section from a certain state.
The edges have two kinds of weights, the change amount of SOC and Fuel consumption.
The value of f(e) is the …
To obtain the value of f(e), we optimize the vehicle control in a section satisfies these constraints.
For example, this orange edge represents that we are able to drive in the section 2 from the state class to while changing the amount of SOC and fuel consumption following the weights of the edge.
And, we prepare the nodes corresponding to the state classes at each section.
Then, we generate the edge which represents the change amount of SOC and fuel consumption when we drive in the section from a certain state.
The edges have two kinds of weights, the change amount of SOC and Fuel consumption.
For example, this orange edge represents that we are able to drive in the section 2 from the state class 𝐻_1 to 𝐻_𝑗 while changing the amount of SOC and fuel consumption following the weights of the edge.

## Slide 19: Local: Optimization of Vehicle Control on a Sections
When should we operate the engine in Driving Cycle?
Where should we set the engine operating point?
When
We generate some simple driving patterns of HV and EV
  There exist at most one continuous HV and EV driving mode in one section
We optimize vehicle control on a section where
SOC is fixed
State cluster at the start and end points are fixed
EV
HV
Section
Notes: To obtain f(e), we have to consider these two important points.
First, we prepare some simple driving patterns of HV and EV mode, because now we consider a short time span of Driving Cycle to obtain vehicle control.
simple driving patterns means

## Slide 20: Local: Optimization of Vehicle Control on a Sections
Region of the engine operating points
Torque
Shaft speed
Where
Approximates the BSI function and which associate Fuel and SOC with a pair of (engine torque, shaft speed) for each driving pattern (We don’t know and because we regard a simulator as a black box)
Solve the NLP with and , and obtain the engine output in HV driving mode as the optimal value of
Approximated function
Sample point data
1. Bicubic Spline Interpolation
2. Non-Linear Problem
Notes: Where should we set the engine operating point?
We use a fact that the engine output and fuel consumption are mainly determined by the engine torque and the engine shaft speed.
Here is the way to determine the engine operating point in HV driving mode.
We use the sample point data in the engine operating region, and based these data, we approximate function using de-Boor algorithm.

## Slide 21: Solving Strategy
Construct State Transition Graph ;
Nodes represent state clusters of vehicle
Edges represent the transitions of the state of vehicle, SOC and fuel consumption in the section
the change amount of
Section
Section
Section
Edge has two type of weight;
SOCFuel
is the objective value of the optimal solution of
Notes: we set f(e) to the objective value of the NLP P.
After generating this State Transition Graph,

## Slide 22: Global: SOC-constrained Shortest Path Problem
objective the summation of Fuel on path minimize constraints 2. initial SOC + (the summation of SOC on path up to the Section n) 3. | the summation of SOC on path| (𝜀 is enough small)
* constraint 1 is taken into consideration at the time of graph construction
objective the fuel consumption minimize
constraints 1. velocity target velocity of Driving Cycle
2. SOC
3. initial SOC final SOC
original problem
SOC-constrained shortest path problem
Notes: we can convert the original problem into the SOC-constrained shortest path problem on this graph.
For example, the objective function of the original problem is converted into the summation of Fuel on path, and
the third constraint is converted into that the absolute value of the summation of SOC on path is enough small.
By using the Edge algorithm, we are able to generate the State Transition Graph. After generating this graph,
we can convert the original problem into the SOC-constrained shortest path problem on this graph.
For example, the objective function of the original problem is converted into the summation of ΔFuel on path, and
the third constraint is converted into that the absolute value of the summation of ΔSOC on path is enough small.

## Slide 23: SOC-constrained Shortest Path Problem (0-1ILP)
initial SOC final SOC
total SOC 0
variable means a path contains edge ⇔
Flow conservation condition Impose constraint to represent the path
Flow conservation
Cumulative Fuel
SOC (any time)
(initial SOC) + sum SOC of section 1 to n
( is the set of edges in the section )
Notes: We formulated SOC-constrained shortest path problem as 0-1 Integer Linear Programming Problem, like flow problem.
We assign a binary variable to every edge and put flow conservation condition.
The flow conservation condition makes the variable becomes 1 when a path contains the edge ,
and becomes 0 when a path does not contain the edge .
We formulated SOC-constrained shortest path problem as 0-1 Integer Linear Programming Problem.
We assign a binary variable 𝑥_𝑒 to every edge 𝑒 and put flow matching condition.
The flow conservation condition makes the variable 𝑥_𝑒 becomes 1 when a path contains the edge 𝑒,
and becomes 0 when a path does not contain the edge 𝑒.

## Slide 24: Outline
Background and Problem Setting
Our Proposed Algorithm
  Local Optimization (Optimize in a part of Driving Cycle)
  Global Optimization (Optimize in a whole of Driving Cycle)
  Reduce Calculation Time
Numerical Experiments
Notes: next,

## Slide 25: Reduction of the Search Space and Calculation Time
Local
Optimize some optimal vehicle controls in a part of the Driving Cycle while changing the conditions
We solve NLP in the local optimization for every edge
Estimate and sieve inefficient edges from the State Transition Graph
 Reduce the local optimization cost
Notes: Next, I explain the reduction of the search space and calculation time
In our proposed algorithm, we solve …

## Slide 26: Reduction of the Search Space and Calculation Time
fixed-SOC-CSP(
Obtain the SOC-constrained shortest path including edge on
variable means a path contains edge ⇔
Estimate and sieve inefficient edges from the State Transition Graph
Notes: we define the fixed-SOC-CSP
this problem obtains
because variable = 1 means a path contains edge
this problem obtains
because variable 𝑥_𝑒 = 1 means a path contains edge 𝑒

## Slide 27: Reduction of the Search Space and Calculation Time
Estimate and sieve inefficient edges from the State Transition Graph
Generate Imitation Graph where are the approximate function of
CSP(
= fixed-CSP }
Construct Sieved State Transition Graph
Length of the SOC-CSP(constrained shortest path) on
fixed- Length of the SOC-CSP including edge on
reducing parameter
Procedure of Sieving Edges
Notes: Let CSP(G) be length …, and let fixed-CSP(G) be …
we generate imitation graph …
define the set of edge satisfies the fixed-CSP(G-tilde, e) ≤ a CSP(G-tilde)

## Slide 28: Reduction of the Search Space and Calculation Time
A result of Sieve Algorithm
# remained edges
/ # edge of Imitation Graph
( = # edge of STG)
Total calculation time
Notes: We succeed the reduce the number of edge, and reduce total calculation time in this table.
the total of (1) and (2) is the time to generate Imitation graph, and
the total of (4) – (6) is the time to generate State Transition Graph

## Slide 29: Outline
Background and Problem Setting
Our Proposed Algorithm
  Local Optimization (Optimize in a part of Driving Cycle)
  Global Optimization (Optimize in a whole of Driving Cycle)
  Reduce Calculation Time
Numerical Experiments
Notes: Finally, I show the result of the numerical experiments

## Slide 30: Result of our proposed algorithm
Case | initial SOC | final SOC | fuel consumption
1 | 16.30 % | 16.30 % | 518.34 g
2 | 12.00 % | 12.01 % | 520.42 g
Driving Cycle: WLTC, SOC lower bound(): 10%
Notes: Finally, we show the result of our proposed algorithm.
This show the 2 case of the result.
We use WLTC Driving Cycle, and we set 𝛽 to 10%, that is the vehicle should always keep SOC above 10%.
Orange Case 1 is the case that started driving with 16.3% SOC.
Blue Case 2 is the case that started driving with 12% SOC.
We succeeded to obtain the car control satisfies the two SOC constraints of the original problem.
One is that Initial SOC and final SOC were nearly equal shown in the table.
And the other is SOC always kept above 10% shown in the fourth figure. This figure shows the transition of SOC of experiments.
The first and second figure shows the transition of engine torque of Case 1 and Case 2, respectively.
Case 2 started driving with 12% SOC, so in order not SOC to fall below 10%, Case 2 drives to charge the battery earlier than Case 1 by increasing the HV driving section.
We conducted experiments under two conditions.
Case one is the case that started driving with 16.3% SOC and color is orange. Case two is the case that started driving with 12% SOC and color is blue.
Driving Cycle is WLTP, and we set 𝛽 to 10%, that is the vehicle always keeps above 10%.
We succeeded to obtain the car control satisfies the two SOC constraints of the original problem.
One is that Initial SOC and target SOC were nearly equal shown in the table.
And the other is SOC always kept above 10% shown in the fourth figure. This shows the transition of SOC of experiments.
The first and second figure shows the transition of engine torque of Case one and two, respectively.
Case 2 started driving with 12% SOC and so that SOC does not fall below 10%, Case 2 drives to charging the battery earlier than Case 1 by increasing the HV traveling section.

## Slide 31: Result of our proposed algorithm
Driving Cycle: WLTC, SOC lower bound(): 10%
Case | initial SOC | final SOC | fuel consumption
1 | 16.30 % | 16.30 % | 518.34 g
2 | 12.00 % | 12.01 % | 520.42 g
initial SOC final SOC
Notes: One is that Initial SOC and final SOC were nearly equal shown in the table.
We conducted experiments under two conditions.
Case one is the case that started driving with 16.3% SOC and color is orange. Case two is the case that started driving with 12% SOC and color is blue.
Driving Cycle is WLTP, and we set 𝛽 to 10%, that is the vehicle always keeps above 10%.
We succeeded to obtain the car control satisfies the two SOC constraints of the original problem.
One is that Initial SOC and target SOC were nearly equal shown in the table.
And the other is SOC always kept above 10% shown in the fourth figure. This shows the transition of SOC of experiments.
The first and second figure shows the transition of engine torque of Case one and two, respectively.
Case 2 started driving with 12% SOC and so that SOC does not fall below 10%, Case 2 drives to charging the battery earlier than Case 1 by increasing the HV traveling section.

## Slide 32: Result of our proposed algorithm
Case | initial SOC | final SOC | fuel consumption
1 | 16.30 % | 16.30 % | 518.34 g
2 | 12.00 % | 12.01 % | 520.42 g
SOC
Driving Cycle: WLTC, SOC lower bound(): 10%
Notes: And the other is SOC always kept above 10% shown in the fourth figure. This figure shows the transition of SOC of experiments.
We conducted experiments under two conditions.
Case one is the case that started driving with 16.3% SOC and color is orange. Case two is the case that started driving with 12% SOC and color is blue.
Driving Cycle is WLTP, and we set 𝛽 to 10%, that is the vehicle always keeps above 10%.
We succeeded to obtain the car control satisfies the two SOC constraints of the original problem.
One is that Initial SOC and target SOC were nearly equal shown in the table.
And the other is SOC always kept above 10% shown in the fourth figure. This shows the transition of SOC of experiments.
The first and second figure shows the transition of engine torque of Case one and two, respectively.
Case 2 started driving with 12% SOC and so that SOC does not fall below 10%, Case 2 drives to charging the battery earlier than Case 1 by increasing the HV traveling section.

## Slide 33: Result of our proposed algorithm
Case | initial SOC | final SOC | fuel consumption
1 | 16.30 % | 16.30 % | 518.34 g
2 | 12.00 % | 12.01 % | 520.42 g
In Case 2, engine have to work in inefficient section to keep SOC ≥ 10%
Driving Cycle: WLTC, SOC lower bound(): 10%
Notes: The first and second figure shows the transition of engine torque of Case 1 and Case 2, respectively.
Case 2 started driving with 12% SOC, so in order not SOC to fall below 10%, Case 2 drives to charge the battery earlier than Case 1 by increasing the HV driving section.
Because of that, the fuel consumption of case 2 is greater than case 1
We conducted experiments under two conditions.
Case one is the case that started driving with 16.3% SOC and color is orange. Case two is the case that started driving with 12% SOC and color is blue.
Driving Cycle is WLTP, and we set 𝛽 to 10%, that is the vehicle always keeps above 10%.
We succeeded to obtain the car control satisfies the two SOC constraints of the original problem.
One is that Initial SOC and target SOC were nearly equal shown in the table.
And the other is SOC always kept above 10% shown in the fourth figure. This shows the transition of SOC of experiments.
The first and second figure shows the transition of engine torque of Case one and two, respectively.
Case 2 started driving with 12% SOC and so that SOC does not fall below 10%, Case 2 drives to charging the battery earlier than Case 1 by increasing the HV traveling section.

## Slide 34: Summarize
(Local) Analyze engine efficiency by Bicubic Spline Interpolation and obtain optimal engine output by solving NLP
(Global) Obtain the state transition of the optimal car control by solving the SOC-constrained shortest path problem on the State Transition Graph formulated as 0-1ILP
Reducing the search space and calculation time by using Imitation Graph
Our algorithm does not depend on simulator and Driving Cycle
Notes: Here is the main points of my presentation.
Thank you for your time and attention.
Do you have any question?